## Slide 1: INDOOR AIR POLLUTION
ProjectSixty Percent
ABHINAV REDDY | 2021101034
ROHIT GOWLAPALLI | 2021101113
GNANA PRAKASH | 2021111027
LSA MOURYA | 2021101121
DATE: 5 -11 -fi 0 fi fi

## Slide 2: Every year, 3.8 million people die from indoor air pollution.
MOTIVATION
S o u r c e : W o r l d H e a l t h O r g a n i z a t i o n
CAUSES
SOLID COOKING FUELS COOLING SYSTEMS
EFFECTS
PREMATURE DEATHS
HEART DISEASES AND CANCER
Necessity is the Mother of Invention

## Slide 3: Indoor Air Quality Statistics in
Source: https://epic.uchicago.in/delhi-homes-record-poor-indoor-air-quality-low- willingness-for-demanding-clean-air/

## Slide 4: Permissible Limits of Air Pollutants
CARBON DIOXIDE
VOLATILE ORGANIC COMPOUNDS
INDEX
Low:
> 250 ppm
Medium: > 1000 ppm
High: > 2000 ppm
Low:
0 - 100
Medium: 101 - 200
High: 200 - 500
Low:
High:
Medium: 50-150
µg/m³
PARTICULATE MATTER
PM 2.5 PM 10
< 50 µg/m³ < 50 µg/m³
50-150
µg/m³
> 150 µg/m³ > 150 µg/m³

## Slide 5: Hardware
Overview
Our Smart IoT-device calculates the levels of various air pollutants such as CO2, particulate matter of sizes 2.5 & 10 microns , VOCs and also measures Heat Index by keeping track of Temperature and Humidity.
ESP32
DHT11/SHT4X sensor Prana-Air CO2 sensor Prana-Air PM sensor PCBs
Power Source
Software
Arduino
ThingSpeak + OM2M Python
React JS + Tailwind CSS
Node JS + MongoDB + Express JS

## Slide 6: PCB DIAGRAM
Sensors used:
Prana Air NDIR CO2 Sensor
SGP40 Sensor (VOC, Temp, Humidity) Prana Air SDS Sensor (PM2.5 and PM10)
CIRCUIT DIAGRAM

## Slide 7: Flow of Information

## Slide 8: Project Flow
Data Handling
Data obtained posted to: ThingSpeak
OM2M
Server
ThingSpeak gives pictorial
representation
OM2M and Server show real-time data
2
3
Wireless node connected to server Measure quantities like:
Temperature and Humidity
CO2 levels
VOC levels Particulate matter
Collected data sent to server
User Experience
Dashboard shows safety levels according to air quality levels
Emails will be sent when air
quality degrades drastically
1 Onsite Implementation

## Slide 9: Data Processing
Calibration
Improper data samples can be ingested since sensors can have different sets of calibration points. To overcome this, we are planning to use Linear Regression to train our project with data samples
Validation & Prediction
Linear Regression through pre-calibrated sensor is employed for validation of the obtained data samples and can ultimately be used to predict future data
Outlier Detection
Routines like Z-score/IQR/boxplot are employed to identify samples that do not fit the expected data distribution.

## Slide 10: Calibration Proper Sensor Calibration yields accurate measurements
Machine Learning
ML is employed to map reference data (used as training data) to experimental data
Linear Regression
LR is used along with plots over numerous data- points ( 1800+ ) collected for more than 24hrs
Identical Trends
The plots are largely similar , but considerable difference in amplitude of reference and experimental plots is observed
Linear Regression Line
Assuming y to be the reading of the reference CO2 sensor and x to be the reading of the uncalibrated sensor, we obtain a relation as y = ax + b where a = 0.896869239565473 and b = 93.18648988932932

## Slide 11: Calibration Curves
Reference sensor is the node deployed in the SPCRC Lab.
The spikes were obtained by lighting incense sticks near the node

## Slide 12: Scatter Plot

## Slide 13: Features of Dashboard
Alerts
Users subscribe to E-mail alerts to get notified when air pollutants rise to hazardous amounts
Live
Displays the latest sensor-wise data with appropriate colour coding where GREEN, ORANGE and RED are used to show values that are in safe, moderate and hazardous levels respectively
Graphs
Displays readings versus time
graphs for different air pollutants and also shows if the node is ONLINE or not

## Slide 14: Dashboard UI

## Slide 15: Dashboard UI

## Slide 16: ALERT SYSTEM MECHANISM

## Slide 17: OM2M
ThingSpeak
Using "ThingSpeak.h" library functions and HTTP Requests through POST-API queries, we data is sent to ThingSpeak into 6 fields where: Field 1 - Particulate Matter 2.5
Field 2 - Particulate Matter 10 Field 3 - Carbon Dioxide
Field 4 - Volatile Organic Compounds Field 5 - Temperature
Field 6 - Humidity
Python script is used to create application entity and containers in OM2M and then data is sent through HTTP requests from the node as container instances which are posted into one of the following containers in the following format:
String cnt[] = {"Prana_PM2.5", "Prana_PM10", "CO2_Levels", "VOC_Levels", "Temperature", "Humidity"}

## Slide 18: Softwares used

## Slide 19: SUMMARY
Email alerts are sent when measured values cross permissible limits Users can access the dashboard via QR Code/URL from any location Our device with the collaboration of other smart IoT devices can form a Smart Home providing an access to easier life in every household Reports can be provided to users every month about the air quality based on the readings taken
Our device can aid in detecting locations that cause excessive harm to the environment.

## Slide 20
WEEK 2
Microprocessor code ThingSpeak and OM2M integration
WEEK 1
Brainstorming
Hardware prototyping Circuit interfacing on Zero PCB
WEEK 4
Calibration Analytics
Validation
ACTION PLAN
WEEK 3
Dashboard
Alert mechanism
Interfacing PM sensor
GOING FORWARD
Ground deployment Management

## Slide 21: DIVISION OF WORK
DASHBOARD & CUSTOM SERVER
ABHINAV REDDY
ROHIT GOWLAPALLI
GNANA PRAKASH
LSA MOURYA
HARDWARE & SENSOR CODE
OM 2 M & THINGSPEAK CODE
DATA ANALYSIS & REPORTS